## Slide 2: Mock Project -Bootloader

## Slide 3: GROUP 3
Nguyễn Hữu Tuấn
Lê Duy Hoàng Minh
Nguyễn Đình Tùng
Leader
Trương Phi Long
Lương Việt Khoa

## Slide 4: LESSION OBJECTIVE 01 03 02 04
Implementation
Principle diagram
Introduce the Bootloader
Bootloader Program

## Slide 5
Bootloader is like a firmware that is loaded into the computer memory and called every time the computer boots
If there is a Bootloader program loaded into the microcontroller, it will first jump into this Bootloader program, do some work then switch to the application program to do it.
1. INTRODUCTION

## Slide 6
Why is Bootloader needed ?
Firmware Update is very important, especially for IoT products
Security, which is absolutely important with embedded/IOT products.

## Slide 7
2. IMPLEMENTATION
1. Hardware and software:
Hardware: Kit FRDM-KL46Z
Software: IAR EW for Arm
2. Firmware
The firmware that we will write here includes the Bootloader program, and two application programs for us to try the firmware update feature.
We can switch between two Firmware by button

## Slide 8
Firmware 2
Firmware 1

## Slide 9
3. Bootloader Program
Reset
Jump Address
Main() function
Get address the current firmware on flash
Bootloader() function
Jump Curent Firmware
Application code
Soft Reset
Super loop

## Slide 10
Specifically about the Bootloader() function
Start
Get address to jump to
Disable all interrupt
Disable Faul Handler
Set main stack point
Set program counter
Jump to application
Get the address of the Firmware to jump to.
Disable system interrupts and clear pending Interrupts, to avoid interrupting the Boot program.
Set MSP - Main Stack Pointer and SCB_VTOR register with the aforementioned effect.
Set PC - Program Counter points to Reset_Handler() of the new Firmware.
Call Reset_Handler() to reset the program. Now, the processor will start with the new Firmware.

## Slide 11
4. Principle diagram
Reset
Delay 5s
Firm 2
Firm 1
Load Firm
SW1
SW2

## Slide 12: Thanks for watching!